## Slide 1: NFC (Near Field Communication) (RFID: Radio Frequency ID)

## Slide 2: NFC (RFID):
Near field communication
Radio frequency identification
Uses software SPI to avoid the limitation in pins
Clock stretching is not supported by hardware I2C
Software SPI uses bit-banging method (i.e. uses GPIO pins HIGH/LOW as data bits)

## Slide 3: NFC (RFID) – PN532 Interfacing
$ git clone https://github.com/adafruit/Adafruit_Python_PN532.git
$ cd Adafruit_Python_PN532
$ sudo python setup.py install
$ cd
$ cd example # your folder
$ mkdir nfc
$ cd nfc
$ sudo nano nfc_test.py

## Slide 4: Python: NFC
import binascii
import sys
import Adafruit_PN532 as PN532
CS = 18
MOSI = 23
MISO = 24
SCLK = 25
pn532 = PN532.PN532(cs=CS, sclk=SCLK, mosi=MOSI, miso=MISO)
pn532.begin()
ic, ver, rev, support = pn532.get_firmware_version()
print('Found PN532 with firmware version: {0}.{1}'.format(ver, rev))
# Configure PN532 to communicate with MiFare cards.
pn532.SAM_configuration()

## Slide 5: Python: NFC (cont.)
print('Waiting for MiFare card...’) while True: # Check if a card is available to read. uid = pn532.read_passive_target() # Try again if no card is available. if uid is None: continue print('Found card with UID: 0x{0}'.format(binascii.hexlify(uid)))

## Slide 6: Block reading (Authentication):
# Authenticate block 4 for reading with default key (0xFFFFFFFFFFFF). if not pn532.mifare_classic_authenticate_block(uid, 4, PN532.MIFARE_CMD_AUTH_B,
[0xFF, 0xFF, 0xFF, 0xFF, 0xFF, 0xFF]):
print('Failed to authenticate block 4!’)
continue
# Read block 4 data.
data = pn532.mifare_classic_read_block(4)
if data is None:
print('Failed to read block 4!')
continue
# Note that 16 bytes are returned, so only show the first 4 bytes for the block.
print('Read block 4: 0x{0}'.format(binascii.hexlify(data[:4])))

## Slide 7: NFC with PHP: