## Slide 1: RASBERRY PI WORKSHOP
By:
Krishna Kumar Sah
E. E. COM.
Firmware Engineer
Real Time Solutions

## Slide 2: Introduction to raspberry pi – 3 (Model B)
The Raspberry Pi is a credit-card sized computer that plugs into your TV and a keyboard, which can be used for many of the things that your average desktop does - spreadsheets, word-processing, games and it also plays high-definition video.
The Raspberry Pi is a charitable foundation.
Maintained by partners as well as opensource community.
• Why so cheap ?
• SoC - System on a chip, a computer on a single low voltage chip
• Linux OS

## Slide 3: Introduction Cont.
Linux on a bootable SD card
  Fedora
  Debian
  ArchLinux
  Windows 10 IOT core
  UBUNTU MATE
  PINET
  RISK OS, etc

## Slide 4: Installation
Step by step installation
Go to https://www.raspberrypi.org/downloads
Main operating used Raspbian
But we use NOOBS (New Out of Box Software), a Raspbian offline installer
Download SD-card Formatter (MAC not required, Linux use gparted)
Format the SD –card using SD-card Formatter
Extract the downloaded file into the SD-card.
Install : Select Raspbian

## Slide 5: Introduction Cont.
By default, supporting Python as the educational language.
Any language which will compile for ARMv6 can be used with the Raspberry Pi, though; so you’re not limited to using Python.
E.g C, C++, HTML, PHP, java etc ..

## Slide 6: Introduction Cont.

## Slide 7: Introduction Cont.
Specifications:

## Slide 8: Introduction Cont.
Key Improvements from Pi 2 Model B to Pi 3 Model B:
  Next Generation QUAD Core Broadcom BCM2837 64bit processor
  Processor speed has increased from 900MHz on Pi 2 to 1.2Ghz
  BCM43438 WiFi on board
  Bluetooth Low Energy (BLE) on board
  Upgraded switched power source up to 2.5 Amps (can now power even more powerful devices over USB ports)

## Slide 9: Introduction Cont.
Other Technical Specification:
  40pin extended GPIO
  4 x USB 2 ports
  4 pole Stereo output and Composite video port
  Full size HDMI output
  CSI camera port for connecting the Raspberry Pi camera
  DSI display port for connecting the Raspberry Pi touch screen display
  Micro SD port for loading your operating system and storing data
  Upgraded switched Micro USB power source (now supports up to 2.5 Amps)
  The same form factor as the Pi 2 Model B, - the only difference is the location of the onboard LEDs

## Slide 10: Introduction Cont.

## Slide 11: Introduction Cont.
The square sapped interface always start with pin number one.

## Slide 12: Remote accessing raspberry pi
Open terminal : Ctrl + alt + t
$ ifconfig
  Show ip address and other details
$ sudo raspi-config
  Opens config window
  (SSL: secure shell)

## Slide 13: Remote accessing raspberry pi

## Slide 14: Remote accessing raspberry pi
Navigate to Interfacing option
  Navigate to SSH (Secure Shell) : for bash
    Enable
      ok
  Navigate to VNC (Virtual Network Computing) : for graphical
    Enable
      Ok
  Finish

## Slide 15: Remote accessing raspberry pi
Finding out Ip address: $ ifconfig
For windows user download PUTTY software
For linux user just type
  Ssh [username]@[ip-address]
    Default username_name : pi
    Default password : raspberry
If unable to connect ssh:
  $ ssh-keygen –R “ip-address-of-ur-pi”
Lots of other bash terminals can be used for ssh
  Windows : putty, bash of git, tera term, etc
  Linux : terminal

## Slide 16: Remote accessing raspberry pi

## Slide 17: Remote accessing raspberry pi (GUI)
We need to remove old vnc server and tight vnc server (clean)
  $ sudo apt-get remove xrdp vnc4server tightvncserver
  $ sudo apt-get autoremove
  $ sudo apt-get autoclean
Install new vnc server
  $ sudo apt-get install tightvncsetver
  $ sudo apt-get install vnc4server
  $ sudo apt-get install xrdp
XRDP shall restart by default if not
  sudo /etc/init.d/xrdp restart
  vncserver :0
(XRDP : remote desktop protocol)

## Slide 18: VNC Viewer:

## Slide 19: Remote Desktop:
For windows search : remote desktop connection (pre-installed)
  If not installed : install
  Enter IP
  Say yes
  User name : pi
  Password : raspberry

## Slide 20
Tera Term:
  Install Tera term:
    Enter ip
    Username
    Password
Bash windows:
  $ ssh pi@192.168.100.166
  $ say yes
  $ password : raspberry

## Slide 21: Update and upgrade
Commands to update and upgrade: (ctrl + alt + t : open terminal)
  $ sudo nano /etc/apt/sources.list
    This will open sources.list file in nano editor
  Go to the line starting with deb and deb-src
    Ctrl + k to remove line
    Copy and lines below:
      deb http://archive.raspbian.org/raspbian jessie main contrib non-free
      deb-src http://archive.raspbian.org/raspbian jessie main contrib non-free
    Ctrl + x to exit and y to save
  $ sudo apt-get purge wolfram-engine
    Since the size is lower we remove wolfram engine (not required)
  $ sudo apt-get autoremove
  $ sudo apt-get dist-upgrade
    This will take little time and say ‘y’ if asked to continue
  $ sudo apt-get update
  $ sudo apt-get upgrade

## Slide 22
Thanks for today …